## Slide 1
KRAKEN QGIS PLUGIN • USER MANUAL
PCI Conflict Checker
Automated spatial overlapping sector detection for identical Physical Cell IDs (PCI) and Modulo collisions across RAN network layers.
Analysis Type
PCI & Modulo 3/6/30
Spatial Engine
Pie Wedge & R-Tree
Output Visual
Polygons & Ray Lines
Kraken © 2026 | akanipatra@gmail.com

## Slide 2
STEP 01 • INPUT CONFIGURATION
PARAMETER & MAPPING SETTINGS
Configure cell layer fields, spatial coverage radius, and select target site types.
01
02
03
Frequency Band & PCI Column
Select targeted frequency band (e.g. 1800) and map PCI attribute column from active GCELL layer.
Distance Radius & Beamwidth
Specify dynamic radius column (e.g. TA) or manual custom distance. Default horizontal Beamwidth is set to 30°.
Site Type Filter Table
Toggle site categories (MACRO, MICRO, PICO, etc.) to include or exclude specific network nodes from detection.
Kraken © 2026 | akanipatra@gmail.com

## Slide 3
STEP 02 • ALGORITHMIC ENGINE
DETECTION MODULO & CALCULATION
Understand collision math and spatial pie wedge intersection geometry.
Fast spatial indexing using QgsSpatialIndex (R-Tree) for instant spatial lookup.
Handles both geographic (WGS84) and projected coordinate reference systems.
MODULO MODES
Conflict Logic Rule
Algorithm screens candidate pairs in current map canvas extent matching specified collision criteria:
GEOMETRY MODEL
Pie Wedge Generation
Synthesizes realistic directional sector wedges based on site coordinates, azimuth, and radius.
•
Same PCI: Direct identical PCI ID collision ( ).
•
Mod 3: PSS (Primary Sync Signal) collision.
•
Mod 6: RS (Reference Signal) pilot pollution.
•
Mod 30: Pattern grouping conflict.
•
Geographic Correction: Auto converts meters to degrees using latitude scale factors.
•
Polygon Intersection: Computes exact spatial overlap geometry ( ).
•
Area Filtering: Filters out zero-area point/line touches.
Kraken © 2026 | akanipatra@gmail.com

## Slide 4
STEP 03 • SPATIAL GIS REPRESENTATION
GIS OUTPUT LAYERS & VISUALS
Automatically rendered conflict layers directly added into QGIS project map canvas.
Orange semi-transparent polygon shapes representing overlapping coverage zones where PCI or Modulo collisions physically occur.
Dotted red connector lines linking serving cell site centroids directly to the conflict zone centroid with automated inline PCI label tags.
1. PCI Conflict Areas Layer
Polygon Layer
2. PCI Conflict Lines Layer
Line Layer
Attribute Table Data: Layers store detailed metadata including Cell A/B IDs, Cell Names, PCIs, Band, and Modulo values.
Kraken © 2026 | akanipatra@gmail.com

## Slide 5
STEP 04 • BEST PRACTICES
EXECUTION & RECOMMENDATIONS
Key operational tips for optimal performance and accurate RAN optimization audits.
SPATIAL FILTER
RADIUS OPTION
SETTINGS MEMORY
Map Canvas Extent
Analysis operates strictly on features within current map canvas bounds for maximum calculation speed. Zoom to cluster area before running.
Dynamic vs Custom Radius
Use TA distance mapping for realistic coverage bounds. Apply fixed Custom Radius (e.g. 1000m) when TA distance field is unavailable.
Auto Memory & Persistence
All dropdown mappings and unchecked site types are automatically saved to QSettings for seamless re-analysis in future sessions.
Kraken © 2026 | akanipatra@gmail.com