## Slide 1
KRAKEN QGIS PLUGIN • USER MANUAL
GCell Generator
High-performance spatial sector geometry engine for large-scale RAN optimization and network visualization in QGIS.
600k+
Rows Processed in Seconds
Multi-Engine
PyArrow, Calamine & GDAL C++
Auto-Styling
GPKG & Dynamic QML Export
Kraken © 2026 | akanipatra@gmail.com

## Slide 2
WORKFLOW PHASE 01
Data Ingestion & Field Mapping
01
02
03
Select Source File
Load cellular dump data via .csv or .xlsx. Accelerated by PyArrow C-Engine and Rust Calamine parser.
Set Coordinates & Azimuth
Map Longitude, Latitude, and orientation columns (Dir & Logical Dir with automatic fallback logic).
Designate Layer Band
Select the Band column to trigger automatic distinct value scanning for multi-layer sector customization.
Kraken © 2026 | akanipatra@gmail.com

## Slide 3
WORKFLOW PHASE 02
Sector Geometry & Symbology Tuning
Auto-Z Index
Coverage Radius
Specify radius in meters per frequency band to visualize cell coverage boundaries effectively.
Beamwidth
Set horizontal aperture width in degrees. Macro cells generate pie wedges; PICO sites form full circles.
Layer Palette
Customize hex fill colors for each band using integrated QGIS color buttons with HSV auto-distribution.
Automated Plot Ordering
Bands are automatically assigned rendering priority to prevent smaller frequency sectors from being hidden under larger ones.
Kraken © 2026 | akanipatra@gmail.com

## Slide 4
WORKFLOW PHASE 03
Generation & Spatial Output
Outputs high-performance spatial databases with native C++ bulk transactions and auto-generated spatial indexes.
Creates paired QML style files matching configured band colors, opacity settings, and rendering order rules.
Instantly imports structured vector layers into the active QGIS project canvas upon completion.
GeoPackage Export (.gpkg)
Spatial Vector
Style File Generator (.qml)
Categorized Symbology
Automatic Canvas Load
QGIS Integration
Kraken © 2026 | akanipatra@gmail.com

## Slide 5
SUMMARY & PERFORMANCE TIPS
Optimization Best Practices
Kraken QGIS RAN Optimization Plugin • GCell Module Engine 3.0
Use CSV Input
For massive dumps exceeding 500k rows, convert .xlsx to .csv to leverage multi-threaded PyArrow processing.
Direction Fallback
Logical Dir is prioritized over physical Dir. Missing azimuths automatically default to 0.0° North orientation.
PICO Cell Handling
Omni-directional PICO sites automatically render as centered circular geometries and take top rendering priority.
Kraken © 2026 | akanipatra@gmail.com