## Slide 1
KRAKEN QGIS PLUGIN • USER MANUAL
Line of Sight (LOS) Analyzer
Interactive GIS clearance tool for evaluating signal propagation paths, terrain DEM profiles, building obstacles, and 3dB vertical beam tilt cones.
Elevation Source
Terrain DEM + OSM Buildings
RF Beam Analysis
Mechanical & Electrical Tilt Cone
Obstacle Detection
Auto Obstacle Coordinates
Kraken © 2026 | akanipatra@gmail.com

## Slide 2
STEP 01 • PARAMETER SETUP
Configure Cell & Receiver Parameters
Map layer fields or assign manual RF values for accurate clearance computation.
Cell Antenna Mapping
Target Receiver (UE) Settings
Field Mapping: Map layer columns for Antenna Height, RS Power, Gain, H/V Beam Width, and Tilts.
Tilt Combination: Automatically sums Mechanical Tilt (M-Tilt) and Electrical Tilt (E-Tilt) for total inclination.
Manual Fallback: Input fixed spinbox values when layer attribute fields are missing.
User Height: Define UE receiver height above ground (default: 1.5m).
Penetration Loss: Set outdoor-to-indoor attenuation factor (dB).
Persistent Memory: Click "Save Mapping" to store defaults permanently in QGIS settings.
Kraken © 2026 | akanipatra@gmail.com

## Slide 3
STEP 02 • MAP INTERACTION
Interactive 2-Point Ray Selection
Simple map canvas selection to trace line-of-sight signal paths instantly.
01
Select Cell Site
Hover and click near any sector wedge on the map canvas. Cursor mode starts as Pointing Hand.
CURSOR FEEDBACK
Hand Cursor → Target Mode
02
Drop UE Target Point
Click target point on map using Crosshair Cursor. Draws red vector line and places UE marker.
CANVAS ACTION
Geodesic Sampling (10m step)
03
Cancel / Reset
Right-click anywhere on canvas to cancel current selection and re-select Cell site.
SHORTCUT
Right-Click to Abort
Auto-identifies closest cell feature.
Auto-populates RF dialog from feature attributes.
Red rubber band line highlights direct path.
Red 'X' marker highlights target UE position.
Clears active lines and UE markers.
Restores default selection state immediately.
Kraken © 2026 | akanipatra@gmail.com

## Slide 4
STEP 03 • PROFILE ANALYTICS
Elevation Profile & Obstacle Inspection
Comprehensive profile plot integrating terrain, structures, and antenna radiation patterns.
Green dashed ray indicates LOS CLEAR. Red ray indicates LOS BLOCKED by terrain/building intersections.
Grey bars display structural height fetched live from OpenStreetMap Overpass API.
Amber shaded cone visualizes vertical 3dB beam coverage based on total tilt angle.
LOS Ray Status
Building Obstacles
3dB Vertical Beam Cone
Kraken © 2026 | akanipatra@gmail.com

## Slide 5
REFERENCE • BACKEND ARCHITECTURE
Elevation & Building Data Pipeline
Multi-tier failover mechanism ensures robust performance even without local raster DEMs.
Local Raster DEM
PRIMARY TERRAIN PROVIDER
OpenTopoData API
FALLBACK TERRAIN PROVIDER
OSM Overpass API
BUILDING HEIGHT ENGINE
Auto-detects DEM layers in active QGIS project.
Supports local DEM, SRTM, and DEMNAS raster formats.
High performance local elevation sampling.
LATENCY
< 100ms (Offline)
Automatic online API fallback if local DEM is missing.
Uses Mapzen elevation dataset in 90-point chunk batches.
Built-in HTTP rate-limit handling & failover.
COVERAGE
Global Mapzen Dataset
Queries OSM ways and relations for building polygons.
Multi-endpoint failover (France, Germany, Kumi).
Parses exact building heights or level counts (* 3.5m).
ENDPOINTS
3 Server Failover Cluster
Kraken © 2026 | akanipatra@gmail.com