## Slide 1
KRAKEN QGIS PLUGIN • USER MANUAL
Best Cell Analyzer
Automated dominant serving cell identification and spatial mesh engine for targeted RAN optimization and coverage troubleshooting in QGIS.
RF Score Engine
Distance & 65° antenna attenuation model
Batch Input
Direct clipboard paste for multiple drop points
Interactive Vector Mesh
Auto-generated styled line & point layers
Kraken © 2026 | akanipatra@gmail.com

## Slide 2
CORE ENGINE • 3GPP ANTENNA MODEL
RF Effective Distance & Scoring
How Kraken identifies dominant serving cells beyond simple geographic distance
Calculates angle difference (0°-180°) between cell azimuth and drop point bearing.
Applies standard model: Attn(dB) = min(20, 12 * (θ / 65)²).
Ranks best servers using weighted RF impact: EffDist = Dist * 10^(Attn / 35).
2x Buffer Auto-Expand
SPATIAL RADIUS FALLBACK
Automatically doubles initial search radius if zero candidates are found in the initial bounding box.
C++ Bounding Box
GEOGRAPHIC & PROJECTED CRS
Utilizes spatial index filtering directly in QGIS C++ engine for instant querying.
01
Angle Deviation (θ)
02
3GPP Antenna Attenuation
03
Effective Distance Score
Kraken © 2026 | akanipatra@gmail.com

## Slide 3
WORKFLOW PHASE 01 • ANALYSIS SETUP
Configuration & Batch Input
Configure ranking criteria and single or batch coordinate drop points
1. Top N Best Cell
Specify maximum serving candidate cells to evaluate (Default: 5, Range: 1-50).
2. Initial Buffer (km)
Define initial spatial search radius in kilometers (Default: 2.5 km).
3. Filter Band / Layer
Select specific frequency layer (e.g., 1800, 2100) or evaluate across ALL BANDS.
4. Excel Copy-Paste Batch Table
Paste multi-row Excel data directly (Name, Longitude, Latitude). Leaves empty for single-click canvas mode.
Kraken © 2026 | akanipatra@gmail.com

## Slide 4
WORKFLOW PHASE 02 • SPATIAL OUTPUT
Map Mesh & Drop Point Rendering
Automatic styling and multi-layer vector generation on QGIS canvas
Red dotted line connection (#FF0055) between drop point and candidate cell centroids. Features automatic distance labels in kilometers.
Multi-ring glowing yellow target marker (#FFFF00) highlighting analysis location with high precision.
Rich Vector Attribute Table
Rank • Tower_ID • Sector • Cell_Name • Band • PRB_Util • Throughput • TA • TA90 • Dist_km • Azimuth • Bearing • Angle_Dev • Attn_dB • Eff_Dist_Score
Layer 1: Best_Cell_Mesh
LineString
Layer 2: Best_Cell_Drop_Point
Point Layer
Kraken © 2026 | akanipatra@gmail.com

## Slide 5
SUMMARY & BEST PRACTICES
Execution Modes & Operational Tips
Maximize workflow efficiency with dual analysis modes and proper setup
AUTO REFRESH
Map-Click Mode
Leave batch table empty. Click OK to activate Crosshair map tool, then click anywhere on canvas for instant single-point analysis.
Batch Excel Mode
Paste hundreds of coordinates directly from Excel. Generates unified batch mesh and drop point layers in a single pass.
Dynamic Column Mapping
Ensure field mappings (Azimuth, Band, Sector, TA, PRB, Throughput) are properly set in Kraken Main Settings prior to running.
Automatic Canvas Cleanup
Re-running analysis automatically refreshes and updates existing Best_Cell_Mesh layers without canvas clutter.
Kraken © 2026 | akanipatra@gmail.com