## Slide 1
KRAKEN QGIS PLUGIN • USER MANUAL
Load Analysis
Automated dual-engine framework analyzing DL PRB Utilization and DL User Throughput to deliver precision Vertical (Cosector) and Horizontal (Inter-site) load balancing targets.
Vertical Engine
Cosector MLB & Coverage Balance
Horizontal Engine
Multi-Tier Spatial Scoring
Pie-Wedge Geometry
60° Beam Intersection Overlap
Kraken © 2026 | akanipatra@gmail.com

## Slide 2
STEP 01 • SYSTEM ARCHITECTURE
Dual Analysis Pipeline Overview
Core Workflow
1. Column Mapping Engine
Resolves user fields via SettingDialog. Extracted without hardcoded aliases across QgsFeature, Pandas Series, and dictionary structures.
Safe Parsing: Handles NULL, N/A, and comma decimals
2. Vertical Load Engine
Evaluates co-sector cells on the same site. Identifies high PRB utilization (>80%) and checks load acceptance against band LTC throughput thresholds.
Outputs: MLB adjustment or Coverage Balancing
3. Horizontal Load Engine
Filters different site towers matching frequency band. Executes spatial cone filtering (45°) and ranks inter-site targets using composite scoring.
Top 5 Inter-Site Candidates Ranking
Kraken © 2026 | akanipatra@gmail.com

## Slide 3
TA90 Ratio | Condition | Recommended Action
< 0.7 | Target coverage shorter | Coverage Balancing
> 1.3 | Target coverage larger | Check MLB Parameter
0.7 - 1.3 | Similar coverage profile | Adjust MLB Target
STEP 02 • VERTICAL ANALYSIS
Cosector Load Balancing Rules
Threshold PRB > 80%
ACTION RECOMMENDATION MATRIX
Trigger 01: High PRB Cell Detection
Identifies cells with PRB utilization exceeding 80%. Flags severe congestion when PRB exceeds 90%.
Trigger 02: Candidate Acceptor Validation
Target cell must satisfy: PRB delta > 30% and throughput meeting/exceeding band LTC threshold.
Trigger 03: Automated Action Logic
Evaluates TA90 coverage ratio between high load cell and acceptor candidate:
Kraken © 2026 | akanipatra@gmail.com

## Slide 4
STEP 03 • HORIZONTAL ANALYSIS
Spatial Cone Search & Iterative Stages
Co-Band Inter-Site Filtering
inter-site_2Km_90degree
Primary dense urban offloading radius inside 45° angle cone.
inter-site_5Km_90degree
Suburban expansion search if Stage 1 yields zero candidates.
inter-site_10Km_90degree
Macro rural fallback boundary for distant neighbor search.
CANDIDATE RANKING MODEL
Total Score Formula
Weighted composite scoring evaluates sector alignment, distance proximity, and coverage overlap.
+
+
STAGE 1
Radius ≤ 2.0 km
STAGE 2
Radius ≤ 5.0 km
STAGE 3
Radius ≤ 10.0 km
40%
Intersection Overlap
60° Pie-wedge Area Ratio
40%
Face-to-Face Alignment
Cos²(d_A) × Cos²(d_B)
20%
Distance Score
Proximity Buffer Scaling
Kraken © 2026 | akanipatra@gmail.com

## Slide 5
STEP 04 • USER INTERFACE & OUTPUT
Load Balancing Analysis Results Window
GUI Execution View
Displays all carrier bands in the sector with TA90, PRB Util (%), and Throughput (Mbps) highlighted by load color codes.
Automated diagnostic messages advising whether to adjust MLB parameters or initiate coverage balancing per cell.
Ranked list showing Distance, Beam Intersect (%), F2F Alignment (%), DistScore, Total Score, target PRB, and Throughput.
1. Cosector Cells Overview
2. Cosector Load Remarks
3. Top 5 Inter-Site Candidates
Kraken © 2026 | akanipatra@gmail.com