## Slide 1
KRAKEN QGIS PLUGIN • USER MANUAL
Coverage Prediction Module
User Manual & System Architecture Guidelines for RSRP Signal Propagation Modeling directly on QGIS Canvas
Propagation Model
5 Different Model Supported
Selection Mode
Interactive Canvas Tool
Visualization
Dynamic & Adjustable RSRP Range
Kraken © 2026 | akanipatra@gmail.com

## Slide 2
SYSTEM ARCHITECTURE
FEATURE OVERVIEW & CORE ENGINE
Simulates and estimates RSRP signal coverage or Path Loss directly within the QGIS workspace. Integrates real-time antenna tilt, sector pattern, power settings, and elevation terrain.
COVERAGE ENGINE WORKFLOW
Non-Modal GUI Dialog: Dynamic setup with window minimize/maximize capabilities.
QGIS Map Tool: Pointing hand tool bound to layer feature identification.
Visual Glow Layering: Triple RubberBand outline glow on map canvas.
CORE PYTHON MODULES
coverage_prediction_dialog.py
Main Qt UI controller, parameters loader, and settings manager.
coverage_prediction_map_tool.py
Canvas map tool handling click identification on Main_GCell vector layer.
selected_cell_predict_*.py
Propagation execution backends (COST-231, Terrain, UMa/UMi, SPM).
Kraken © 2026 | akanipatra@gmail.com

## Slide 3
WORKFLOW STEP 01
INTERACTIVE CELL SELECTION
GUI Control Dialog with Auto-Populated Parameters
01
02
03
ACTIVATE MAP TOOL
Set Prediction Type to Selected Cell. The cursor transforms into a Pointing Hand on map canvas.
CLICK TARGET SECTOR
Click any sector wedge on GIS map canvas. The system identifies the nearest feature from layer.
MULTI-LAYER GLOW EFFECT
Selected cell geometry is highlighted with 3-tier RubberBand glow (Outer Cyan Halo, Mid Aura, Solid White Core).
Main_GCell
Kraken © 2026 | akanipatra@gmail.com

## Slide 4
WORKFLOW STEP 02
GENERAL SETTING PARAMETERS
PROPAGATION MODEL
Select signal attenuation algorithm:
CLUTTER CATEGORY
Defines environmental loss environment:
BAND CONFIGURATION
Map sector frequency bands dynamically:
Automatically queries distinct values from selected field (e.g. 850, 1800, 2100 MHz).
PREDICTION METRIC
Switch prediction calculation target:
• RSRP / Rx Level (dBm) • Path Loss (dB)
GRID & RESOLUTION
Configure grid step and radius:
Resolution: 10x10, 20x20, 50x50m Max Distance: 2 Km, 5 Km, 10 Km, 20 Km
OBSTACLE DATA
Incorporates line-of-sight obstacles:
• Terrain Only (DEM) • Terrain + Building (DSM)
•
COST-231 Hata
•
Path-Specific Terrain
•
UMa & UMi Model
•
Standard Propagation
•
Free Space Path Loss
Dense Urban
Urban
Sub Urban
Rural
Kraken © 2026 | akanipatra@gmail.com

## Slide 5
Parameter | Target Mapping | Fallback Keywords
Height | Antenna Height (m) | height, antenna_height, hgt
RS Power | TX Power (0.1 dBm) | rs_power, power, tx_power
Antenna Gain | Gain (dBi) | antenna_gain, gain, ant_gain
Beams (H/V) | 3dB Beamwidth (°) | hbeam, vbeam, bw_h, bw_v
Tilts (M/E) | Mechanical & Electrical | m_tilt, e_tilt, mech_tilt
WORKFLOW STEP 03
CELL & RECEIVER CONFIGURATION
CELL FIELD AUTO-MAPPING
The plugin auto-detects sector attributes from the vector layer based on smart keyword matching:
RECEIVER CONFIG
In Selected Cell mode, numerical input fields remain fully editable, allowing users to perform custom "What-If" tilt or power adjustment simulations.
User Height (m)
1.5 m (Default)
Penetration Loss
0 dB (Outdoor)
Kraken © 2026 | akanipatra@gmail.com

## Slide 6
PROPAGATION INTELLIGENCE
SUPPORTED PROPAGATION MODELS
COST-231 HATA MODEL
Standard Urban / Sub Urban
Extended Hata model suited for cellular communications between 1500 MHz to 2000 MHz. Calculates path loss based on base station height, mobile height, and urban density factors.
PATH-SPECIFIC TERRAIN MODEL
Hilly / Mountainous Terrain
Extracts terrain elevation profiles along the radio path directly from DEM rasters to compute diffraction loss over obstacles and mountain ridges.
3GPP UMA & UMI MODELS
Urban Macro / Micro
3GPP TR 38.901 standard propagation model for 5G NR and 4G LTE. Differentiates between Urban Macro (high BS elevation) and Urban Micro (street canyon level).
STANDARD PROPAGATION MODEL (SPM)
Calibrated Macro Cells
Empirical formulas tuned for general macro cell planning, balancing diffraction, clutter attenuation, and distance slope factors.
Kraken © 2026 | akanipatra@gmail.com

## Slide 7
WORKFLOW STEP 04
EXECUTION & SIMULATION RENDERING
Path-Specific Terrain Model RSRP Heatmap Visualization
TRIGGER SIMULATION
Click the bold Predict button at the bottom of the dialog. The plugin processes raytracing, 3D pattern attenuation, and path loss equations.
DYNAMIC HEATMAP LAYER
Generates a temporary memory raster/grid layer on the QGIS map canvas styled with standard RF color gradations (Blue = Excellent RSRP, Green = Good, Orange/Red = Edge Coverage).
TERRAIN SHADOWING OUTPUT
Notice how the predicted heatmap respects terrain contours, creating natural signal blockages and hill shadows on the satellite backdrop.
Kraken © 2026 | akanipatra@gmail.com

## Slide 8
URBAN COVERAGE EXAMPLE
DENSE URBAN PREDICTION (TERRAIN + BUILDING DSM)
Dense Urban Prediction (Terrain + Building DSM Model)
BUILDING SHADOWING & DIFFRACTION
When Terrain + Building (DSM) is enabled, signal loss accounts for urban building heights, causing sharp attenuation behind high-rise structures and along street canyons.
MICRO-CELL CLUTTER INTERACTION
High-resolution prediction grids capture fine-grained signal drops across dense building blocks while reflecting main lobe dominance from the target sector antenna.
MULTI-SECTOR INTERFERENCE CONTEXT
Overlaid GCell sector wedges clearly illustrate serving sector alignment versus surrounding neighbor cells in high-density metropolitan zones.
Kraken © 2026 | akanipatra@gmail.com

## Slide 9
OPERATIONAL CHECKLIST
BEST PRACTICES & TROUBLESHOOTING
VERIFY VECTOR LAYER
Ensure is correctly set in Kraken Settings before launching the tool.
CHECK TERRAIN DATA
For Path-Specific Terrain predictions, verify that DEM/DSM rasters are loaded in the current QGIS project.
GRID RESOLUTION OPTIMIZATION
Use 50x50 resolution for fast macro-cell checks, and 10x10 resolution for precise urban dense simulations.
main_gcell_layer_id
Kraken © 2026 | akanipatra@gmail.com